## Slide 1: R Programming for Geospatial Applications

## Slide 2: Outline
Handling spatial data in R
Join tables (join table to shapefile)
Select features (select by attribute)
Buffer (shapefile), unionSpatialPolygons
Zonal statistics as table (for Raster data)

## Slide 3: Join tables (join csv table to shapefile)

## Slide 4: Join tables (join csv table to shapefile)

## Slide 5: Joining CSV to Shapefile Using sf Library
Steps to Join CSV to Shapefile
library(sf) library(dplyr) # Load the shapefile watershed <- st_read("watershed.shp") # Read the CSV file agstats <- read.csv("agstats.csv")
# Assuming both data frames have a common key named "Subbasin" joined_data <- left_join(watershed,agstats,by='Subbasin') # Display the first few rows of the joined data names(joined_data)
## [1] "OBJECTID.x" "GRIDCODE" "Subbasin" "Area" "Slo1" ## [6] "Len1" "Sll" "Csl" "Wid1" "Dep1" ## [11] "Lat" "Long_" "Elev" "ElevMin" "ElevMax" ## [16] "Bname" "Shape_Leng" "Shape_Area" "HydroID" "OutletID" ## [21] "OBJECTID.y" "MEAN" "geometry"
# Plot the joined data plot(joined_data["MEAN"])

## Slide 6: Outline
Handling spatial data in R
Join tables (join table to shapefile)
Select features (select by attribute)
Buffer (shapefile), unionSpatialPolygons
Zonal statistics as table (for Raster data)

## Slide 7: Example (select by attribute)
Each point has columns (i.e., ‘V’) indicating storm surge height
storm <- st_read('stormsub.shp')
## Reading layer `stormsub' from data source ## `/Users/yshao/work/Geog4254-5254G/week3/stormsub.shp' using driver `ESRI Shapefile' ## Simple feature collection with 203 features and 4 fields ## Geometry type: POINT ## Dimension: XY ## Bounding box: xmin: -76.222 ymin: 36.556 xmax: -75.88 ymax: 36.929 ## Geodetic CRS: GCS_unknown
plot(storm['V'])

## Slide 8: Select points based on user-defined threshold value? (e.g, >1.6m)
storm_new <- storm[storm$V>1.6,] plot(storm_new['V'])

## Slide 9: Outline
Handling spatial data in R
Join tables (join table to shapefile)
Select features (select by attribute)
Buffer (shapefile), unionSpatialPolygons
Zonal statistics as table (for Raster data)

## Slide 10: Buffer (shapefile)
library(terra) dem<-rast('dem.tif') stream<-st_read('stream.shp')
## Reading layer `stream' from data source ## `/Users/yshao/work/Geog4254-5254G/week3/stream.shp' using driver `ESRI Shapefile' ## Simple feature collection with 69 features and 17 fields ## Geometry type: LINESTRING ## Dimension: XY ## Bounding box: xmin: 1533018 ymin: 1908419 xmax: 1570308 ymax: 1939364 ## Projected CRS: NAD_1983_Albers
plot(dem) plot(stream,add=T)

## Slide 11: Add 90m buffer
buffer_90m <- st_buffer(stream, dist = 90) plot(dem) plot(stream,add=T) # Plot the buffer on top of the DEM and stream plot(buffer_90m, add=TRUE, border='blue')

## Slide 12: Vary buffer size based on stream attribute
# Create varying size buffers based on stream$Wid2 buffers <- st_buffer(stream, dist = stream$Wid2 *10) plot(dem) # Plot the buffers on top of the DEM and stream plot(buffers, add=TRUE, border='red')

## Slide 13: Outline
Handling spatial data in R
Join tables (join table to shapefile)
Select features (select by attribute)
Buffer (shapefile), unionSpatialPolygons
Zonal statistics as table (for Raster data)

## Slide 14: st_union function
plot(st_geometry(watershed))

## Slide 15
# Use st_union to merge polygons merged_watershed <- st_union(watershed) plot(merged_watershed)

## Slide 16: Outline
Handling spatial data in R
Join tables (join table to shapefile)
Select features (select by attribute)
Buffer (shapefile), unionSpatialPolygons
Zonal statistics as table (for Raster data)

## Slide 17: Zonal stats as table
Mean elevation for each block group?
Other examples?

## Slide 18: Example
dem <-rast('dem.tif') plot(dem) watershed <- st_read('watershed.shp')
## Reading layer `watershed' from data source ## `/Users/yshao/work/Geog4254-5254G/week3/watershed.shp' using driver `ESRI Shapefile' ## Simple feature collection with 69 features and 20 fields ## Geometry type: MULTIPOLYGON ## Dimension: XY ## Bounding box: xmin: 1530828 ymin: 1904204 xmax: 1570308 ymax: 1942124 ## Projected CRS: NAD_1983_Albers
plot(st_geometry(watershed),add=T)

## Slide 19
zonal_stats <- terra::extract(dem, watershed, fun = mean, na.rm = TRUE)

## Slide 20: Zonal stats (example)
zonal_stats <- terra::extract(dem, watershed, fun = mean, na.rm = TRUE) head(zonal_stats)
## ID dem ## 1 1 201.4263 ## 2 2 257.2389 ## 3 3 144.3227 ## 4 4 152.8894 ## 5 5 124.1636 ## 6 6 146.2609

## Slide 21: Zonal stats (example)
watershed_dem <- cbind(watershed, zonal_stats) head(watershed_dem)
## Simple feature collection with 6 features and 22 fields ## Geometry type: MULTIPOLYGON ## Dimension: XY ## Bounding box: xmin: 1547058 ymin: 1932284 xmax: 1564038 ymax: 1942124 ## Projected CRS: NAD_1983_Albers ## OBJECTID GRIDCODE Subbasin Area Slo1 Len1 Sll Csl ## 1 1 1 1 846.63 7.159707 7479.260 60.95703 2.8819298 ## 2 2 2 2 1275.48 11.582822 9096.427 60.95703 3.6230700 ## 3 3 3 3 1689.84 6.194226 6712.752 60.95703 1.0154209 ## 4 4 4 4 954.27 8.749758 6970.326 60.95703 1.7553535 ## 5 5 5 5 539.01 8.037927 4734.335 60.95703 1.1133784 ## 6 6 6 6 4287.33 7.089381 17598.185 60.95703 0.8703648 ## Wid1 Dep1 Lat Long_ Elev ElevMin ElevMax Bname ## 1 4.647356 0.3055068 39.14776 -77.77326 204.5456 148 365 <NA> ## 2 5.942838 0.3599257 39.13989 -77.79659 246.9485 148 503 <NA> ## 3 7.035534 0.4027927 39.12110 -77.68260 142.4591 100 177 <NA> ## 4 4.993355 0.3204881 39.11078 -77.64879 150.8887 104 235 <NA> ## 5 3.544441 0.2550246 39.09038 -77.68311 123.4939 90 168 <NA> ## 6 12.299908 0.5845452 39.10363 -77.73203 148.7355 92 249 <NA> ## Shape_Leng Shape_Area HydroID OutletID ID dem ## 1 17760 8466300 300001 100001 1 201.4263 ## 2 23100 12754800 300002 100002 2 257.2389 ## 3 24540 16898400 300003 100003 3 144.3227 ## 4 19980 9542700 300004 100004 4 152.8894 ## 5 14700 5390100 300005 100005 5 124.1636 ## 6 45000 42873300 300006 100006 6 146.2609 ## geometry ## 1 MULTIPOLYGON (((1552398 193... ## 2 MULTIPOLYGON (((1550358 193... ## 3 MULTIPOLYGON (((1558308 193... ## 4 MULTIPOLYGON (((1562448 193... ## 5 MULTIPOLYGON (((1558308 193... ## 6 MULTIPOLYGON (((1555818 193...

## Slide 22: Zonal stats (example)
plot(watershed_dem['dem'])