## Slide 1: Working with remote sensing image using R

## Slide 2
NASA Earth Observatories
Number of Satellites?
2500+

## Slide 3
Remote Sensing Data Analysis
Land Cover map: use of remote sensing techniques
Notes: definitions of categories and data collection methods by source agencies, incomplete data coverage, varying data age, and employment of incompatible classification systems

## Slide 4
Remote Sensing-derived map products

## Slide 5
Urban surface temperature
Algae bloom mappping

## Slide 6
Download Landsat data; Import data to Rstudio
Vegetation index (Normalized Difference Vegetation Index or NDVI)
Normalized Difference Water Index
Image classification (land cover mapping)

## Slide 7
https://glovis.usgs.gov/app?fullscreen=0

## Slide 8
Demo

## Slide 10
Download Landsat data; Import data to Rstudio
Vegetation index (Normalized Difference Vegetation Index or NDVI)
Normalized Difference Water Index
Image classification (land cover mapping)

## Slide 11
Vegetation Indices
Normalized Difference Vegetation Index (NDVI)
NDVI: [-1.0, 1.0]
Often, the more the leaves of vegetation present, the bigger the
contrast in reflectance in the red and near-infrared spectra.

## Slide 12: Normalized Difference Vegetation Index (NDVI)
NDVI =(NIR - R) / (NIR + R)
In Landsat 4-7, NDVI = (Band 4 – Band 3) / (Band 4 + Band 3)
In Landsat 8, NDVI = (Band 5 – Band 4) / (Band 5 + Band 4)

## Slide 13: Normalized Difference Water Index
For Landsat 7 data,
NDWI = (Band 2 – Band 5) / (Band 2 + Band 5)
For Landsat 8 data,
NDWI = (Band 3 – Band 6) / (Band 3 + Band 6)

## Slide 14
Download Landsat data; Import data to Rstudio
Vegetation index (Normalized Difference Vegetation Index or NDVI)
Normalized Difference Water Index
Image classification (land cover mapping)

## Slide 15
Image classification approaches - computer-aided classification
Themes can vary (examples):
Urban, forest, ag, wetland, .. (NLCD)
Soil, vegetation, impervious surface, water
Computer algorithms (many)
- ML (Maximum Likelihood Classification)
- CART (Classification and regression trees)
- Random Forest Algorithm

## Slide 16: Image classification applications
Deforestation
Urban mapping and urban growth mapping
Coastal wetlands vegetation
Precision Agriculture
Identify invasive species
..

## Slide 17
Supervised Classification Algorithms
Users provide the computer with some examples (training pixels)
of known features in multi-dimensional feature space.

## Slide 18
Supervised Classification Algorithms
Band 3
Band 4
Forest
Ag
Urban
Generate statistics
for supervised classification

## Slide 19
Twoclass.shp (urban and forest polygons)

## Slide 21
Maximum Likelihood Classification
In a two dimensional spectral space, each class form a probability density region,
the probability for a pixel belongs to a center category is defined by its distance
measured in standard deviation. The pixel is assigned a class that is most likely
(maximum likelihood).
Disadvantages: Large number of computations, particularly many spectral bands
are involved.

## Slide 23
Supervised Classification Algorithms in ENVI

## Slide 24
Test different image classification algorithms
Band1
Weights
Weights
Forest
Non-forest
Band2
Band3
Band4
…．
Band4
Class2
Band4>95
Band3<50
SVM
CART
Neural Networks
Classification and Regression Tree
Random Forest
Support Vector Machine
Class1

## Slide 25
Image classification (land cover mapping)
Training data polygons (e.g., urban, forest, ag…)
Landsat image
Dataframe of training data
Classcode (y) | Band3 (red) | Band4 (nir)
1 | 13000 | 15000
1 | 12500 | 18321
2 | 9800 | 4560
2 | 9832 | 4780
1 | 14500 | 19200
1 | . | .
1 | . | .
1 | . | .
1 | . | .
1 | . | .
1 | . | .
3 | . | .
3 | . | .
3 | . | .
1 | . | .
1 | . | .
Y~ f(x)
(classification problem,not a regression)

## Slide 26
Twoclass.shp (urban and forest polygons)

## Slide 27
Y~ f(x)
(classification problem,not a regression)
Classcode (all pixels) | band1 | band2
? | 14000 | 12000
? | 13500 | 18521
? | 1900 | 3560
? | 4832 | 3780
? | 4500 | 9200
? | . | .
 | . | .
 | . | .
 | . | .
 | . | .
 | . | .
 | . | .
 | . | .
 | . | .
 | . | .
 | . | .
Make predictions for all pixels

## Slide 28
Twoclass.shp (urban and forest polygons)

## Slide 29
Rscript and demos