## Slide 1: Terrain Analysis with the terra Package in R
Slope, Aspect, Hillshade

## Slide 2: Introduction
The 'terra' package in R is a powerful tool for handling and analyzing spatial data, including raster data for terrain analysis.

## Slide 3
library(terra)
dem <- rast(‘dem.tif’)

## Slide 4: Calculating Slope
Calculate the slope using the 'terrain' function. Slope is the steepness or degree of incline of a surface:
slope <- terrain(dem, v = 'slope', unit = 'degrees')

## Slide 5: Calculating Aspect
Calculate the aspect using the 'terrain' function. Aspect is the compass direction that a slope faces:
aspect <- terrain(dem, v = 'aspect', unit = 'degrees')

## Slide 6: Calculating Hillshade
Calculate the hillshade using the 'shade' function. Hillshade is a 3D representation of the surface with shadows:
hillshade <- shade(slope, aspect, angle = 45, direction = 0)

## Slide 7
Visualize the results:
par(mfrow = c(2, 2)) # Arrange plots in a 2x2 grid
plot(dem, main = 'DEM')
plot(slope, main = 'Slope')
plot(aspect, main = 'Aspect')
plot(hillshade, main = 'Hillshade')

## Slide 8: Additional Terrain Analysis
Other terrain attributes can be computed using the 'terrain' function by changing the 'v' argument:
Roughness: terrain(dem, v = 'roughness')
Topographic Position Index (TPI): terrain(dem, v = 'TPI')
Terrain Ruggedness Index (TRI): terrain(dem, v = 'TRI')